## Slide 2
WAIKATO
REGIONAL COUNCIL
Lake Taupo Zone Committee
02 August 2019
Waikato region: - Climate change in context

## Slide 3: National and regional emissions
Waikato regional emissions – 2015 / 2016 year by sector in RED
75%
17.2% | GHG emissions
10% | Land area
9.6% | Population
8.4% | GDP
Notes: Waikato makes up:
8.4% of NZ GDP
9.6% of NZ Population
9.1% of NZ exports
26.2% of NZ dairy cows
25.3% of NZ milk solids production
30.7% of NZ dairy herds
25.5% of NZ ha in dairy production
14.8% of NZ forestry and logging GDP
29.1% of NZ dairy farming GDP
13.3% of NZ dairy manufacturing GDP
13.3% of NZ dairy GDP (farming and manufacturing combined)
All from Infometrics
In the year to June 2016, activities within Waikato Region’s boundaries generated 13.8 million tonnes of carbon dioxide equivalent (tonnes CO2e). When forestry is included, the total net emissions are reduced to 8.2 million tonnes CO2e. This compares with national gross emissions of 80.2 million tonnes CO2e The Waikato region’s contribution to gross national emissions in 2016 was therefore 17.2 percent, a relative reduction of 18 percent from 2002 levels.
Agricultural activities in the region generate the largest amount of the gross emissions (75.5 percent), followed by transportation (11.7 percent) and stationary energy (9.7 percent). Forestry removed a net volume of 5.6 million tonnes CO2-e or 41 percent of the total gross emissions.
http://www.mfe.govt.nz/climate-change/state-of-our-atmosphere-and-climate/new-zealands-greenhouse-gas-inventory
Compared to 2002 – Waikato region was 21% of national emissions profile (reduced 18% - expansion of Ag in other regions and close down of 2 Rankine units in Huntly (coal to gas))

## Slide 4: Climate change projections and impacts
Varies with season and spatially over time (2014, IPCC, AR5 CMIP5 data)
Less frosts in the north of the region
More intensive rain events in the south and west of the region - higher flows to west coast harbours – lake Taupō and Waipa sub catchments
Less wind average but higher winds speeds during storm events
Similar average rainfall in the north-eastern part of the region – shift in delivery with late summer rainfall events and increased droughts
Notes: The IPCC's Fifth Assessment Report (AR5) relies heavily on the Coupled Model Intercomparison Project, Phase 5 (CMIP5), a collaborative climate modelling process coordinated by the World Climate Research Programme (WCRP).

## Slide 5: Government Directions
  Regional development
    1Billion trees
  Shift in Transport priorities
    Mode shift to rail, public transport, walking
  New zero emissions target for 2050
  Establishment of an Interim Climate Change Committee
    National Climate Change Risk Assessment Framework
    National Adaptation Plan
    Roadmap of 5 yearly carbon budgets
    ETS review

## Slide 6: ETS – NZ Emission Unit price
30 July 2019 $ 23.50

## Slide 7: Climate Change Responses: Mitigation or Adaptation or both?
“Climate mitigation is about carbon emissions, climate adaptation is about water”
14 January 2016

## Slide 9: Adaptation as a transition – starting now - Forever

## Slide 10: Water
Too much water – floods – land use change
Not enough water – water allocation increased storage
Sea level rise / Coastal & groundwater
Manage for extremes

## Slide 11
Tairua River 2002

## Slide 12
Morrinsville, March 2013

## Slide 13
Scotsman’s Valley, Waikato March 2013

## Slide 14
Thames Coast 05 January 2018

## Slide 15
Whitianga: Highest storm tide (Current) + locked – in 0.4m SLR
www.waikatoregion.govt.nz/coastal-inundation-tool/
Notes: Released live 02 March 2016
Purpose is to identify low lying coastal areas
Inundation modelling at 0.2 m increments based on LiDAR
Interactive Web Based mapping
User able to map inundation extent of water level elevations
Additional information to provide indicative scenarios for:
Tides - Storm tides & Sea Level Rise
Provide the public with a ‘heads up’ in identifying possible inundation issues in the future.
www.waikatoregion.govt.nz/coastal-inundation-tool/

## Slide 16: Carbon sequestration: Right tree, Right place, Right purpose
Focus on carbon sequestration may favour and direct afforestation towards P. radiata
Would not be suitable in all applications
Some land would suit other species or native protection planting
Regeneration of natives may be an even better option
Enhanced property scale riparian plantings would deliver co-benefits:
  Enhanced water quality
  Biodiversity
  Reduced bank erosion
  Aquatic habitat protection,
  Flood attenuation and
  Carbon sequestration

## Slide 17: Opportunities
Waikato region has 523,000 ha marginal land* in pasture (2012)
Current use is mostly dry stock and dairy support
Could be used for mix of production (447,00ha) forestry and protection (76,000ha) plantings
65,000ha only of ‘commercial’ land
Co-benefits for water quality and estuarine habitat
* LUC Classes VIe, VII & VIII

## Slide 18
Tolaga Bay 05 June 2018

## Slide 19
Tolaga Bay 05 June 2018
Notes: King Tide examples

## Slide 20
Hunua Ranges January 2017

## Slide 21: Waikato region –carbon sequestration opportunities using natives
80% shrubs, 20% trees, 75% survival
1ha, 1000 stems: 205.4 tonnes CO2 after 50 years
50% shrubs, 50% trees, 75% survival
1ha, 1000 stems: 337.8 tonnes CO2 after 50 years
Notes: 100% trees @75% survival = 558.4 tonnes CO2 after 50 years

## Slide 22: Way Forward
Can’t do it alone – Work with Iwi partners, stakeholders, businesses and communities
Understand local climate projections and impacts
Understand local greenhouse gas emissions Establish the science base
Measure corporate emissions
Understand exposure of current activities to climate impacts
Understand local issues – seek local solutions
Factor climate projections into all long term decision-making
Reduce exposure to carbon e.g. through procurements /contracts
Embed low carbon and climate awareness into corporate culture – policies, recruitment, systems, templates, training, rewards.
Review and amend external policies, rules and design / operation of infrastructure

## Slide 23: Influences and Responses
Bringing it all together in the WRC context

## Slide 24
Thank you
Ngā mihi
Notes: 100% trees @75% survival = 558.4 tonnes CO2 after 50 years